C1, C2, & C3 Ignition Coil Testing

The ignition coil in C1-3 Corvettes is sometimes the culprit when your car won’t start.  The coil transforms (multiplies) the low voltage that it receives from the cars electrical system.  It increases the voltage to many thousands of volts each time the breaker points open and close.  The coil has two windings, the primary winding, a slot iron core and a secondary winding.  Each time the rotor strikes a spark plug wire contact within the distributor the coil sends a high voltage pulse of current to that spark plug.  If you don’t get the high voltage pulse, your car won’t start.

So if your starter keeps cranking and you have checked that fuel is properly flowing, it’s time to check the ignition system.  Testing for spark is nothing new.  Simply pull a spark plug from the engine or, even better, use a spare plug by inserting it in one of your cars plug wires that you have pulled off a spark plug.  Hold it so that the base of the spark plug is against grounded against the engine block, usually the head, and have someone crank the engine over.

Caution:  Ensure that you hold the plug wire and spark plug with a well insulated glove or well insulated tool.

The gap in the plug should show a bright blue spark jump across the gap each time that plug fires as the engine is cranked.  If you see no spark or very little spark, it’s time to check the coil.

See the next page for this simple process.

C1, C2, & C3 Ignition Coil Testing